## Slide 1: Creating Simulation Results PDFs
June 17, 2025

## Slide 2: Report Generation - Summary
**Note – This process can be run on your PC.
Empty folders: _out_files and _extracted
Copy contingency output folders to _out_files folder
Run extract.py
Edit Graph_configuration.xlsx to set up channels
Run plot_2025_05_9.py
Open Test6.pdf

## Slide 3: First Time User…
There are a few python modules that need to be installed.
Download and install python 3.11
  https://www.python.org/downloads/release/python-3110/
  Choose the custom installer and
    select the location to be c:\Program Files\Python311
    Also select the option to add to environment variables, which means you will not need to add in the next step.
Confirm that PIP is in your path.
  Open command window in Admin mode
  $echo %PATH%
    If you do not see C:\Program Files\Python311\Scripts in the PATH then you need to add it.
    Open system environment and add C:\Program Files\Python311\Scripts to the PATH system variables (in Admin mode)
      Find path in the system variable list, highlight and then edit. You can use the browse button to find the C:\Program Files\Python311\Scripts directory

## Slide 4: First Time User…
    Browse to find C:\Program Files\Python311\Scripts
    Reboot

## Slide 5: First Time User…
  In the command window
    $pip install numpy
    $pip install pandas
    $pip install openpyxl
    $pip install natsort
    $pip install tabulate
    $pip install matplotlib
    $pip install fpdf
    $pip install pyPDF2
  Now you can run the python files to create the reports.

## Slide 6: Reporting Scripts Folder

## Slide 7: Test Output files
Prepare folders in Reporting scripts
  Delete files from _out_files
  Delete files from _extracted
After you have run the DMAT_PSCAD script, the RESULT folder will have an output folder for each test.
Copy these new test output folders to _out_files folder
Open and Run extract.py using idle3.11
This script will convert the out files into a .npz format with a file with index lookup table with the channel information.

## Slide 8: Configure Channels
Open one of the Test_####_lookup.txt files
Use this to determine channel information to complete columns M and O in the Graph_configuration excel sheet.
Open Graph_configuration .xlsx

## Slide 9: Graph_configuration.xlsx
Column | Notes
B | Set to 1 if you want to include the plot in the report
D | Notes
E, F | Rows, Cols - Used to set up the placement of the plots on the page
G, H | Row, Col – Used to assign the channel to a particular plots
L | Range – Leave blank to plot the full simulation time. You can also specify a smaller range to zoom in.
K, M, O | These are channel identifiers taken from Test_####_lookup.txt file
N | Unit for the Y axis
P | Plot title

## Slide 10: Report Generation
Empty folders: _out_files and _extracted
Copy test output folders to _out_files folder
Run extract.py
Edit Graph_configuration.xlsx to set up channels
Run plot_2025_05_9.py
Open test6.pdf

## Slide 11: Report Generation
Prepare Folders
Run extract.py
Configure EXCEL file
Run Plot script
Empty folder _out_files
Empty folder _extracted
Steps to create a report from PSCAD tests
Copy test out files
Generates a lookup table
Edit Graph_configuration.xlsx to set up channels
Run plot_2025_05_9.py
Test6.pdf

## Slide 12: PQ Capability Curve Plot
Ensure that the appropriate test results (Test 51 to 56) out files have been extracted by following the steps outlined previously.
Run the “PQ Capability Curve” script. For BESS, open the “PQ Capability Curve” script and uncomment the lines specified in the script.
The relevant graphs will be plotted and saved in the Report Generation folder.